## Slide 1: Using Rvfpga Practically
Luke Seed
30th May 2024

## Slide 2: Environment
There is no perfect environment in which to work and to develop RVfpga-based applications
  Win
  MacOS
  Linux
However, one is better than the other
  Linux
This can be a dual-boot Linux box OR a Linux VM
Let’s Assume you will be using Linux and that you are going to use Ubuntu 18 or 20 (either will work fine)

## Slide 3: Ubuntu VM
If you have not got the capacity to dual-boot a computer and install Ubuntu in a partition then you may need to go down the VM route
VM stands for Virtual Machine and, typically, it means running a guest operating system on another host machine within an application (hypervisor)
There are various VM applications but a good, free one is VirtualBox
*
VirtualBox will not run on M based Macs but Boot Camp does (paid for)

## Slide 4: Requirements
Your Linux ‘box’ needs at least 8Gb of RAM and should have circa 100Gb disk
If you are using VirtualBox then these things can be set when you create your VM but to give the VM 8Gb of RAM you will need at least 16Gb of RAM in your computer
Once you’ve set up your Linux box you are good to go
  Remember – when you install Linux to set yourself up as a user with admin rights and REMEMBER the password you use (you will need it periodically)

## Slide 5: Git Repository
The RVfpga data has now been set up on a remote Git Repository:
https://github.com/Microelectronic-Group-MISS-TUoS/RVFPGA_MSc_Project.git
To set up the Rvfpga directory you need to clone the repository on your local machine
  Open a terminal and cd/mkdir to a directory where you want the data to land and enter git clone https:://github.com/Microelectronic-Group-MISS-TuOS/RVFPGA_MSc_Project.git
  Enter the directory cd RVFPGA_MSc_Project/
  Before you start any editing, enter git checkout –b MyBranchName
  (This will create a new branch and any changes you make will be associated with the branch and not affect the main repository, main)

## Slide 6: Storing Changes Remotely
Once you’ve edited anything in your branch you can upload it to the remote Git Repository
This doesn’t alter main (until we want it to) but it makes the changes available to other collaborators
To do this, firstly, commit any changes to the local version of the repository git commit –a -m ‘a helpful message saying what changes you made’
Then push the changes back to the remote repository git push –u MyBranchName

## Slide 7: Getting Started
Follow the Rvfpga Getting Started Guide
This will lead you through installing
  Visual Studio Code/Platform IO (the development environment)
  Vivado (for Verilog code synthesis)
  Verilator (for simulation)
  GTKwave (for viewing simulation results)
However, you will probably need to install a few more things
  g++ Version 10.5 (a legacy version of gcc)
  gedit (a good window based text editor)
If you Google it, you will find out how to do it
*
Vivado does have its own simulator but it generates errors if you try to simulate Rvfpga. Verilator, however, is more tolerant

## Slide 8: Vivado
To synthesise Rvfpga for FPGA you need version Vivado 2019.2
This is more than 3 years old now
The preferred method for installing Vivado is the SelfExtracting Web Installer but this won’t work for 2019.2
Instead, you will need to download the Unified Installer. This is a TAR/GZIP file
  Download it
  Extract it using tar –xvf <tarfile>. This will create a new directory with a whole bunch of files in it
  Navigate to the directory and run xsetup
  Select WebPack to install and enter the credentials you set up to identify that you are a valid user

## Slide 9: Vivado and Ubuntu
When you try to install Vivado on Ubuntu it will report a lack of compatibility if you are using anything more recent than Ubuntu 18
I have not noticed and issues using Ubnutu 20 but an installation on Ubuntu 22 might require some additional library installs
sudo apt install libtinfo5
sudo apt install libncurses5
Followed by a restart

## Slide 10: Alternatively …
If you are running your VM on a Win machine you can …
create a smaller VM
Install Vivado on Windows
You will need, within Virtual Box, to specify a shared directory (shared between the host OS – Windows and the guest OS – Linux)
  This is a folder that appears in both Windows and Linux and will allow you to share data between your computer and Linux
  Put the Rvfpga folder into the shared folder – now both OSs can access the data

## Slide 11: Verilator
Verilator is an application that analyses all of your Verilog code and uses it to create a bunch of C++ program files (along with some other code.
Having done this a C compiler/linker is then used to build an executable application (Vrvfpgasim)
Vrvfpgasim IS the simulator – when it is runs it generates the results of the simulation in a vcd file (Value Change Dump) – which you can then view
The code generated by Verilator needs to be compiled using gcc version 10.x – this is a legacy version

## Slide 12: Building the Simulation
The building of the simulation is dne in verilatorSIM/ and is controlled by a Makefile
make is a utility that allows you to selectively generate files based on when things have changed. It allows you to identify dependencies between files and how to generate the dependent file – this is only done if the modify date on the dependent file is earlier than the modify date on any file used to generate it
By default, make looks for a file called Makefile and does what it says

## Slide 13: The Make process
All that Makefile in verilatorSIM/ does is to say
  Vrvfpgasim depends on Vrvfpgasim.mk and is generated by running make on Vrvfpgasim.mk (using some specified options)
  Vrvfpgasim.mk is generated by running Verilator using swervolf_0.7.vc
swervolf_0.7.vc (Verilog Configuration) has two parts:
  At the top are a bunch of +incdir+ and –CFLAGS –I statements (these identify directories to be included by verilator – and the C compiler)
  Below this is a long list of .v and .sv files – these are the Verilog files making up your design
  This is, essentially, a recipe for building RVfpga

## Slide 14: The Choice of Compiler
The default version of GCC tools in Ubuntu will not work to compile the simulator
Firstly, install gcc/g++ version 10 – these, by default, will be gcc-10/g++-10
Now, if you look in Vrvfpgasim.mk two variables are used to identify the compiler and linker
  CXX and LINK
These are actually defined in $(VERILATOR_ROOT)/include/verilated.mk
  VERILATOR_ROOT is defined at the top of Vrvfpgasim.mk
Edit this file and where you find CXX=g++ and LINK=g++, edit these to CXX=g++-10 and LINK=g++-10
Now, when the make process runs, version 10 of the compiler will be used

## Slide 15: Using the Built Design
Rvfpga is a processor system – when it operates (on the FPGA or in simulation) the processor needs to be running a program that is compiled/assembled into R-V object code and placed in the processor’s RAM
Typically, you will develop your source program (C or assembler) in VSC and then build your program:
  Click on the PlatformIO icon
  Click on Build in the Project Tasks menu
Where does the resultant object code go and how is it loaded into the processors RAM?

## Slide 16: Code Project Directory
To build code, create a new PlatformIO project and place it in a new directory (under Rvfpga/examples/MyProj say)
Write your code and build it
Within Rvfpga/examples/MyProj there is a hidden directory (Ctrl-H to unhide it) called .pio/
Navigate to Rvfpga/examples/MyProj/.pio/build/swervolf_nexys/
Here you will find a bunch of files called firmware.x – these are your compiled object code
Edit firmware.dis (this is a textual disassembly of your code)

## Slide 17: Object Code
firmware.dis will look like
Disassembly of section .text.init:
00000000 <_start>:
0: b0201073 csrw minstret,zero
4: b8201073 csrw minstreth,zero
8: 4081 li ra,0
a: 4101 li sp,0
c: 4181 li gp,0
e: 4201 li tp,0
10: 4281 li t0,0
firmware.vh will look like
  It’s a bunch of 64 bit hex numbers
  In little-endian format
B8201073B0201073
4201418141014081
4401438143014281
4601458145014481
4801478147014681

## Slide 18: FPGA or Simulation
There are two top-level Verilog modules
  Rvfpganexys for synthesis to operate on an FPGA
  Rvfpgasim for simulation
Why?
The answer lies in what’s inside the design and what isn’t
Nexys A7
SDRAM
FPGA
rvfpganexys
JTAG
FPGA
Host PC
Memory model
rvfpgasim
Swervolf_core
Simulation

## Slide 19: Running Code on FPGA
When a design is to be implemented on FPGA. The physical design will be in rvfpganexys.bit (generated by synthesizing and P&R the design in Vivado)
Clicking on the Upload Bitstream button in in the PlatformIO menu downloads rvfpganexys.bit to the Nexys board and it begins running but there is no program to run
Now clicking on the Upload button downloads firmeware.vh to the Nexys board and loads it into the RAM at address 0
This is done via the JTAG port
Now resetting and releasing the R-V processor from reset will run the program that is now in memory

## Slide 20: Running Code in Simulation
In the top-level module for simulation there is some code that uses Verilog semi-hosting functions (these generally allow the simulation to access the host computer’s file system)
$readmemh(file, mem) loads a file consisting of a list of hex numbers (e.g. firmware.vh) into an array of reg inside your design – the memory model
Clicking on Generate Trace in the PlatformIO Project Tasks menu will run the simulation and the results will be put into .pio/build/swervolf_nexys/trace.vcd
Host PC
Memory model
rvfpgasim
Swervolf_core
Disk
Firmware.vh

## Slide 21: Running a Simulation Manually
Click on Generate Trace will, in most cases, be enough to run your simulation
However, the default simulation will finish after circa 400ns and this may not be enough
You can run your simulation for longer by doing it manually:
  Firstly (after building your code), click on Generate Trace (this will ensure that firmware.vh exists and is up-to-date)
  Secondly, in a Terminal, cd to your project directory (say Examples/MyProj)
  Finally, enter the following command in the Terminal:
  ../../verilatorSIM/Vrvfpgasim –ram_init_file=./.pio/build/swerv_nexys/firmware.vh –vcd=1 –timeout=TIMEOUT
  Where TIMEOUT is how long you want the simulation to run, in ps (i.e. if you want 1us of simulation, TIMEOUT=1000000)

## Slide 22: Putting It All Together
When you download Rvfpga/ there is a default rvfpganexys.bit file
  Until you change the Verilog you don’t have to rebuild this
  The existing one will run code
You do have to build Vrvfpasim and one you’ve set the tools up it’s as simple as opening a terminal, changing directory to verilatorSIM/, typing make clean (to clean out any previous build) and then make to build Vrvfpgasim
You can the build a software project in Visual Studio Code

## Slide 23: If You are Simulating
Have Visual Studio Code open with your project
Have a terminal open at verilatorSIM/
If you are editing the Verilog code, have a text editor open with the files you are editing
When you are ready to run a simulation
  If you’ve changed your C code then Build it and just Generate Trace
  If you’ve changed your Verilog code then use the terminal to rebuild the simulation and then Generate Trace in Visual Studio Code
Navigate to .pio/build/swervolf_nexys and double click on trace.vcd
  This should open GTKwave
  You can then navigate the design hierarchy and select signals to view
  Don’t close this when you go back and make edits – when you’ve re-simulated just use Menu->File->Reload Waveform to dump the new results in GTKwave
Loop back and repeat until your design is correct
Rinse- and- Repeat

## Slide 24: Linux 1.01
Get used to using Terminal in Linux and entering text commands
  Yes, it’s ‘old school’ but sometimes it’s the only way
Common Linux commands
  cd – change directory (~/ is your home directory, .. Is enclosing directory, / is the separator)
  ls - list directory contents
  pwd – where am I
  sudo <command> (run <command> with admin rights – you may be asked for your password)
  tar (create or expand an archive: tar –cvf tarfile directory/ archives the directory’s contents into tarfile, –cvzf compresses it tar –xvf tarfile extracts the contents of tarfile)
  git (allows you to access a remote repository git clone repository makes a local copy of a remote repository - repository will be a URI if the repository is on a remote system
  apt (allows you to install or update software e.g sudo apt install package)
  grep (search for string/regex in files) e.g. grep –r ‘my cat’ * will list all instances of the string, “my cat” in any file inside the current directory or sub directory